## Slide 1: PAI-Ped / PAI-Walker / πPed A hybrid pedestrian behavior model for AV testing in Simulation

## Slide 2: Hybrid Crossing Model Components
C-GAN
Noisy Transformer
Starting section
Finishing section
Mid section
What?
Combines social-force-based approach and machine learning-based approach.
A generative model that navigates a pedestrian while crossing.
A model that can act in unseen scenarios, while acting plausibly in seen scenarios.
Why?
Force-based approach is not expressive. They learn a very simple function that produces a limited variety. Trajectories are highly predictable. One model cannot capture cultural and road diversity.
ML-based approaches learn from existing non-representative data, so, cannot adapt well to unseen situations. Highly expressive, but fails due to lack of data.
RQs:
Is it feasible to combine force-based and deep-learning approaches to generate interactions and capture real-world trajectories? That is, can we adjust the trajectories generated by a data-driven machine learning model to an emergent scenario using force-based models?
Can the hybrid model capture behavior not captured with force-based models and deep-learning models? We want to show that the hybrid approach has more expressiveness than individual approaches.
Evaluation in the unseen scenarios:
Against Deep Social Force
Against the Social-forced-based model
Against Social-GAN
Forced-Transformer

## Slide 3: Effective Crosswalk Area Modeling for Pedestrians in Simulation-based AV Testing.

## Slide 4: Crosswalk Area model
Effective Area
Designed Area
Effective Area
Designed Area
Effective Area
Designed Area
Effective Area
Designed Area
What: Real-world pedestrians cover an area different from designed crosswalks. The area is even wider when they jaywalk. We model the crosswalk area so that pedestrian behavior models can generate trajectories.
Usage:
Can be used to measure the area coverage of pedestrian crossing models.
Can be used by predictive models (AV) to measure areas of interest in addition to forecasting trajectories.
Can be used by generative crossing models to increase diversity of trajectories.
RQ:
Do the existing crossing behavior models cover the real-world envelope?
Does our approach cover the effective cross-walk area as the real-world scenarios?
Evaluation:
Evaluating generated polygons against the ground truth (difference with the ground truth that closely represents the generated, average area comparison, area distribution comparison)
Variation in ground truth given the same environment
Relative positional heat-map.
Integration of the model with PAI-Ped.